## Slide 1: Getting Started

## Slide 2: Github
All the Arduino programs required for the workshop are on:
https://github.com/GRIETIOTLAB
- Go to GISMO-V repository
Go to GettingStarted folder
GISMO5_OnboardLED.ino

## Slide 3: Hello World
Blinking an LED
Onboard LED connected to pin 2
Create a new project in Arduino
Copy raw content of GISMO5_OnBoardLED.ino into the file
Compile and name file as LED
Upload onto GISMO-V board via USB port
Onboard LED

## Slide 4: Hello World
#define onBoardLED 2
void setup()
{
pinMode(onBoardLED , OUTPUT);
}
void loop()
{
digitalWrite(onBoardLED , HIGH);
delay(1000);
digitalWrite(onBoardLED, LOW);
delay(1000);
}

## Slide 5: Hello World
Select ESP32 Arduino -> ESP32 Dev Module as the Board
Select the COM port to which your bard is mapped

## Slide 6: Relay module
ESP32
13

## Slide 7: Relay module
#define relayPin 13
void setup(){
pinMode(relayPin,OUTPUT);
}
void loop(){
digitalWrite(relayPin,HIGH);
delay(2000);
digitalWrite(relayPin,LOW);
delay(2000);
}
Path:
github.com/GRIETIOTLAB/GISMO_V/GettingStarted/GISMO5_relay.ino

## Slide 8: Relay module
GISMO-V
Line
Neutral
Normally open (NO) contacts are brought out onto terminal blocks
On relay switching on, the NO contacts will close and the Line circuit will be complete and the bulb will glow

## Slide 9: Magnetic switch
GND
Internal pullup
Mag sw
ESP32
GPIO16

## Slide 10: Magnetic switch
#define magSW 16
void setup() {
pinMode(magSW,INPUT_PULLUP);
Serial.begin(115200);
}
void loop() {
int sw_status;
sw_status = digitalRead(magSW);
if (sw_status)
Serial.println("Switch open");
else
Serial.println("Switch closed");
delay(1000);
}

## Slide 11: OLED display
OLED: Organic Light Emitting Diode
OLED display pin | ESP32 pin
GND | GND
VCC | 3.3V
SCL | GPIO22
SDA | GPIO21
I2C

## Slide 12: OLED display
Feature | Value
Screen size | 0.96 inches
Internal controller | SSD1306
Color displayed | Blue
Resolution | 64 x 128
VCC | 3.3V
Protocol | I2C

## Slide 13: OLED Display
#include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3C,21,22);
I2C address
SDA,SCL

## Slide 14: OLED Display
display.init();
display.setFont(ArialMT_Plain_24);
display.clear();
display.drawstring(0,0,”Hello World”);
display.display();
c
c

## Slide 15: WiFi
ESP32 acts as a station and gets connected to a WiFi router

## Slide 16: WiFi
#include <WiFi.h>
#define WIFI_SSID “xxxxxxxxxxxxxxxxxx”
#define WIFI_PASSWORD “xxxxxxxxxxxxxxxxxxxxxx”
The SSID (Service Set Identifier) is the name of your wireless network, also known as Network ID. This is viewable to anyone with a wireless device within reachable distance of your network. ... The SSID is the name of your wireless network. This is what you will look for when connecting wireless computers and devices.

## Slide 17: WiFi
WiFi.begin(WIFI_SSID,WIFI_PASSWORD);
Serial.print(“Connecting to WiFi”);
while(WiFi.status() != WL_CONNECTED)
{
Serial.print(“.”);
delay(300);
}
Serial.print(“Connected with IP:”);
Serial.print(WiFi.localIP());

## Slide 18: Firebase
#include <FirebaseESP32.h>
#define FIREBASE_HOST “xxxxxxxxxxxxxxxxxxxxxxx”
#define FIREBASE_AUTH “xxxxxxxxxxxxxxxxxxxxxxx”
FirebaseData firebaseData; // Firebase data object

## Slide 19: Firebase
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.reconnectWiFi(true);
Firebase.setFloat(FirebaseData, “IOTLAB/My_App/Sensor_Value”,value);
delay(2000);
Pushing sensor data to Firesbase file : GISMO5R_Firebase.ino
c
c

## Slide 20: Firebase
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.reconnectWiFi(true);
String ledCmdFull;
String ledCmd;
Firebase.getString(FirebaseData, “IOTLAB/My_App/Motor_Cmd”,ledCmdFull);
ledCmd = ledCmdFull.substring(2,ledCmdFull.length()-2);
finalCmd = ledCmd.toInt();
delay(2000);
Pulling command data from Firesbase file : GISMO5R_Firebase_CR.ino
c
c