## Slide 1: IEEE Skill Connect - IoT Level 2 – Train the Trainers
Using the IEEE Starter Kit

## Slide 2: Agenda
1
Introduction to IoT, IEEE Starter Kit;
Sensor Interfaces
2
Ambient parameter Monitoring, Smart Lock, Range Meter
3
4
5
Smart Garden, Home Safety & Security
6
Intro to AWS
Environment Monitoring, RTC based Control, Fall Detection
Cloud database creation , Interface to Starter Kit
6
Mobile App Development Framework

## Slide 3: Internet of Things - IOT
A system of internet-connected ‘things’ that can collect and transfer data over a wireless network without human intervention
Information
Control

## Slide 4: IOT Applications
Intrusion detection
Door/Window open
LPG Gas Leak detection
Appliance Control
Soil moisture
Temperature, humidity, leaf wetness sensing
Watering schedules
Industrial IOT
Manufacturing plants
Process plants

## Slide 5: IOT @ IEEE Skill Connect
IEEE Starter Kit
Mobile
Cloud
IOT eco-system
Sensors
Data acquisition board
Internet connectivity
Web services
UI using mobile app

## Slide 6: Project Building Blocks
Sensor/ Actuator interface
Sensor data processing
Internet connectivity
Cloud database interface
Mobile App
Ambient parameter monitor
Environment monitor
Range meter
Audio meter
Motor control
Biometric lock control
Smart garden

## Slide 7: Project Building Blocks
Sensor Interface
Serial
Parallel
Analog
Digital
I2C
SPI

## Slide 8: Project Building Blocks
Data Processing
Limit checking
Engg. unit conversion
Peak-to-peak computation
Local display

## Slide 9: Project Building Blocks
Internet connectivity & Cloud database
Joining WiFi network
Connection status to Internet
Data access from cloud database

## Slide 10: Project Building Blocks
Mobile App Development
UI Design
Cloud database interface
Periodic update

## Slide 11: IEEE Starter Kit
Resources
ESP32 DevKitC
DHT11 :Temperature and humidity sensor
Relay
Polarized connectors for:
  OLED graphic display
  BME280 Environment sensor
  MPU6050 3-axes accelerometer & gyro
  Soil moisture sensor
  RTC DS3231 module
  HC-SR04 Ultrasonic sensor
  MQ6 LPG Gas leak sensor
  Magnetic sensor

## Slide 12
Sensor Pack
Soil moisture sensor
BPM280 Environment sensor
HC-SR04 Ultrasonic sensor
MPU6050 3-axes accelerometer & gyro
DS3231 Real Time Clock
Magnetic switch
MQ6 Gas leak sensor
OLED graphic display

## Slide 13: ESP32 Dev Kit
ESP-WROOM-32: 32-bit microprocessor
I/O pins: These pins are capable of Digital Read/Write, Analog Read/Write, PWM, IIC, SPI, DAC and much more.
Micro-USB jack: The micro USB jack is used to connect the ESP32 to our computer through a USB cable. It is used to program the ESP module as well as can be used for serial debugging as it supports serial communication
EN Button: The EN button is the reset button of the ESP module.
Boot Button: Press and upload program from Arduino IDE
Red LED: The Red LED on the board is used to indicate the power supply.
Blue LED: The Blue LED on the board is connected to the GPIO pin2.

## Slide 14: Inside the ESP32

## Slide 15: ESP32 features
ESP32 has Xtensa® Dual-Core 32-bit LX6 microprocessors. The ESP32 will run on breakout boards and modules from 160Mhz upto 240MHz
Internal Memory : 448 KB ROM for booting and core functions & 520 KB SRAM for data and instructions
External Flash : 4MB external Flash extendable to16MB
WiFi: ESP32 implements TCP/IP, full 802.11 b/g/n/e/i WLAN MAC protocol
Bluetooth : ESP32 supports the latest BLE Bluetooth 4.2, as well as classic Bluetooth

## Slide 16: ESP32 peripherals
GPIO
Timers and Watchdog
Real Time Clock
ADC and built-in Sensors
Digital to Analog Convertor (DAC)
Touch Sensor
Ultra Low Power(ULP) Co-processor
Ethernet MAC Interface
Universal Asynchronous Receiver Transmitter (UART)
I2C Interface
I2S Interface
SPI Interface
Pulse Width Modulation (PWM)

## Slide 17: ESP32 – powering & programming

## Slide 18: Preparing Arduino IDE for ESP32
STEP 1: Now, let’s get started. The first step would be to download and install the Arduino IDE.. If you already have one make sure it is of the latest version.
STEP 2: Once installed, open the Arduino IDE and go to Files -> Preferences to open the preferences window and locate the “Additional Boards Manager URLs:” as shown

## Slide 19: Preparing Arduino IDE for ESP32
STEP 3: This text box might be empty or might also contain some other URL if you have used it previously for ESP8266. If it is empty simply paste the below URL into the text box
https://dl.espressif.com/dl/package_esp32_index.json

## Slide 20: Preparing Arduino IDE for ESP32
STEP 4: Now go to Tools -> Boards -> Board Managers to open the Board manager window and search for ESP32.
If the URL was pasted correctly your window should find the below screen with Install button, just click on the Install button and your board should get installed.

## Slide 21: Preparing Arduino IDE for ESP32
STEP 5: Make sure you have an active internet connection and wait while the installation gets complete. It may take few minutes based on the speed of your internet connection.

## Slide 22: Programming ESP32 with Arduino
STEP 1: Connect your ESP32 board to your computer through the micro-USB cable. Make sure the red LED goes high on the module to ensure power supply.
STEP 2: Start the Arduino IDE and navigate to Tools -> Boards and select ESP32 Dev board as shown

## Slide 23
STEP 3: Open device manager and check to which com port your ESP32 is connected to. Mine is connected to COM 8 as shown

## Slide 24: ESP32 – Arduino IDE
In the Tools tab, go to
Board -> ESP32 Arduino -> ESP32 Dev Module
In the Tools tab, go to
Port-> COMX

## Slide 25: Arduino IDE
pinMode(2,OUTPUT);
pinMode(3,INPUT);
pinMode(4,INPUT_PULLUP);
2
4

## Slide 26: The Arduino IDE
digitalRead ()
digitalWrite ()
analogRead ()
analogWrite()
Analog
Digital
Input
Output

## Slide 27: Your first program
void setup(){
pinMode(2,OUTPUT);
}
void loop(){
digitalWrite(2,HIGH);
delay(1000);
digitalWrite(2,LOW);
delay(1000);
}
Press the Boot button and upload

## Slide 28: Relay operation
ESP32
19
void setup(){
pinMode(19,OUTPUT);
}
void loop(){
digitalWrite(19,HIGH);
delay(2000);
digitalWrite(19,LOW);
delay(2000);
}

## Slide 29: Ambient Parameter Monitoring using IoT
Parameter | Range | Accuracy
Ambient Temperature | 0 – 50 degrees C | +/- 2 degrees
Relative Humidity | 20-90 % | +/- 5%
Update Rate : 2 seconds

## Slide 30: DHT11
DHT11 | ESP32
VCC | 3.3V
DATA | GPIO27
NC | NC
GND | GND
GISMO-V connections
Ckt. Details:
DATA pin pulled up to VCC with a 5.6K resistor

## Slide 31: DHT11
The DHT11 is a basic, low cost digital temperature and humidity sensor.
DHT11 is a single wire digital humidity and temperature sensor, which provides humidity and temperature values serially with one-wire protocol.
DHT11 sensor provides relative humidity value in percentage (20 to 90% RH) and temperature values in degree Celsius (0 to 50 °C).
DHT11 sensor uses resistive humidity measurement component, and NTC temperature measurement component.

## Slide 32: Sensor interface
DHT11 uses only one wire for communication. The voltage levels with certain time value defines the logic one or logic zero on this pin.
The communication process is divided in three steps, first is to send request to DHT11 sensor then sensor will send response pulse and then it starts sending data of total 40 bits to the microcontroller.

## Slide 33: Communication with microcontroller
Response
To start communication with DHT11, first we should send the start pulse to the DHT11 sensor.
To provide start pulse, pull down (low) the data pin minimum 18ms and then pull up, as shown in diag.
Start pulse ( Request)
After getting start pulse from, DHT11 sensor sends the response pulse which indicates that DHT11 received start pulse.
The response pulse is low for 54us and then goes high for 80us.

## Slide 34
Output
After sending the response pulse, DHT11 sensor sends 40(5 bytes) bit data output
First 2 bytes: Humidity in %
Next 2 bytes: Temperature in C
Last byte: Checksum
End of frame

## Slide 35: Code from basics
void request(){
pinMode(27,OUTPUT);
digitalWrite(27,LOW);
delay(20);
digitalWrite(27,HIGH);
}
Start pulse ( Request)
void response(){
pinMode(27,INPUT_PULLUP);
while(digitalRead(27) == HIGH);
while(digitalRead(27) == LOW);
while(digitalRead(27) == HIGH);
}

## Slide 36
byte receive_data(){
byte c = 0;
for(int i =0;i < 8;i++){
while (digitalRead(27) == LOW);
delayMicroseconds(30);
if(digitalRead(27) == HIGH){
c = (c<<1) |(0x01);
}
else
c = (c<<1);
while(digitalRead(27) == HIGH);
}

## Slide 37: Sensor Interface with library