## Slide 1: IoT Projects
Using GISMO-V board

## Slide 2: Smart garden
Monitor soil moisture
Get threshold from Firebase
Compare with threshold
Switch on motor if dry else switch off
Transfer soil moisture and pump status to
  OLED display
  Firebase database

## Slide 3: Smart Garden
Soil Moisture sensor | ESP32 pin
VCC | 3.3V
A0 | GPIO34
D0 | NC
GND | GND
The soil moisture sensor provides a digital as well as a analog output. We will be using the analog output

## Slide 4: ADC in ESP32
ESP32 has 2 12-bit ADCs – ADC1 and ADC2
ADC1 – 8 channels – GPIOs 32 – 39 (GPIO34 is used)
ADC2 – 10 channels – GPIOs 0,2,4,12-15, 25-27
12 bit ADC:
I/P analog voltage | ADC value
0V | 0
3.3V | 4095

## Slide 5: Location on board
Soil moisture sensor is connected via a polarised 4-pin connector cable to the board

## Slide 6: Basic read
#define smPin 34
#define relayPin 13
pinMode(13,OUTPUT);
Serial.begin(115200);
int val = 4095 – analogRead(smPin);
if( val < threshold) digitalWrite(relayPin,HIGH);
else digitalWrite(relayPin,LOW);
Note: Check sensor reading with water and without water and fix threshold

## Slide 7: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 8: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.getString(firebaseData,”IOTLAB/Smart_Garden/SM_Threshold”,s);
s1 = s.substring(2,s.length()-2);
threshold = s1.toInt();
Firebase.setInt(firebaseData,”IOTLAB/Smart_Garden/Soil_Moisture”,sm);
Firebase.setString(firebaseData,”IOTLAB/Smart_Garden/Motor_Status”,”ON”

## Slide 9
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(0,0,soilMoisture);
display.drawstring(0,30,motorStatus);
I2C address
SDA, SCL

## Slide 10: Mobile App

## Slide 11: Fall Detector
Detect position of object:
  Upright
  Fallen Left
  Fallen Right
  Fallen Forward
  Fallen Backward
Transfer object position to:
  OLED display
  Firebase database

## Slide 12: MPU6050
MEMS 3-aixs accelerometer and 3-axis gyroscope values combined.
Power Supply: 3-5V.
Communication : I2C protocol.
Built-in 16-bit ADC provides high accuracy.
Micro-electromechanical systems (MEMS) is a process technology used to create tiny integrated devices or systems that combine mechanical and electrical components.

## Slide 13: MPU6050
MPU6050 pin | ESP32 pin
VCC | 3.3V
GND | GND
SCL | GPIO22
SDA | GPIO21
I2C

## Slide 14: MPU6050 data
Sensitivity : +/- 2g
Output : 16 bit
+/-2g corresponds to +/-32767
1g corresponds to 32767/2 = 16384
Dividing the accelerometer value by 16384 will give the value in g

## Slide 15
Location on board

## Slide 16
#include “I2Cdev.h”
#include “MPU6050.h”
#include “Wire.h”
MPU6050 mpu;
mpu.initialize();
mpu.read();
IOT Lab, ECE Department
void mpu_read(float *ax,float *ay,float *az){
int16_t _ax,_ay,_az,_gx,_gy,_gz;
mpu.getmotion(&_ax,&_ay,&az,&_gx,&_gy,&_gz);
*ax = _ax/16384.0;
*ay=_ay/16384.0;
*az=_az/16384.0;
}
Use the Serial Plotter in the ArduinoIDE to visualize the acceleration in the three axes

## Slide 17: Calibration
There is a calibrate function which is called in setup(). In this function 10 acceleration values in the X,Y and Z directions are taken and averaged and the average value is taken as the baseline value. This baseline value is subtracted from the actual read value
void calibrate()
{
float ax,ay,az;
for(int i=0;i < 10;i++)
{ mpu_read(&ax,&ay,&az);
delay(100);
}
baseline[0]=ax;
baseline[1]=ay;
baseline[2]=az; }

## Slide 18: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 19: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.getString(firebaseData,”IOTLAB/Fall_Detector/Limit”,s);
s1 = s.substring(2,s.length()-2);
limit = s1.toFloat();
Firebase.setInt(firebaseData,”IOTLAB/Fall_Detector/Position”,position)

## Slide 20
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(30,0,”Position:”);
display.drawstring(30,30,position);
I2C address
SDA, SCL

## Slide 21: Mobile App

## Slide 22: Range Finder
Use an ultrasonic sensor to find out the range of an object
Transfer the range value to:
  Local OLED display
  Firebase database in the cloud
Develop mobile app in Kodular
  Display of range value in app – text as well as graphical

## Slide 23: Ultrasonic sensor

## Slide 24: Ultrasonic sensor
ESP32
Potential divider
5V operation
3.3V operation

## Slide 25: Ultrasonic sensor
Ultrasonic sensor | ESP32 pin
VCC | 5V
Trigger | GPIO25
Echo | GPIO26
GND | GND

## Slide 26
Location on board

## Slide 27: Ultrasonic sensor – basic read
pinMode(trigPin,OUTPUT);
pinMode(echoPin, INPUT);
digitalWrite(trigPin,HIGH);
delayMicroseconds(10);
digitalWrite(trigPin,LOW);
t = pulseIn(echoPin,HIGH);
distance = t x 0,034/2;
delay(1000);
t is in microcseconds
t in seconds = duration/1000000
Distance travelled in 1 second = 340 x 100 cm
Distance travelled in time t = t x 340 x100/1000000
= t x 0.034
This is the distance to and from the object
Range = t x 0.034/2

## Slide 28: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 29: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.setInt(firebaseData,”IOTLAB/Range_Meter/Range”,range);

## Slide 30
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(0,0,range);
display.display();
I2C address
SDA, SCL

## Slide 31: Mobile App