## Slide 1: IoT Projects
Using GISMO-V Board

## Slide 2: Motor Control
Mobile app with Start and Stop buttons
Transfer Start and Stop commands to Firebase
From GISMO-V read the motor commands
Take action as per commands
Mobile App
Firebase
GISMO-V

## Slide 3: Motor Control

## Slide 4: Motor Control
Tag value in Firebase: IOTLAB/Motor_Control/Motor_Cmd

## Slide 7: Motor Control
GISMO-V
Line
Neutral
Contactor
Motor

## Slide 8: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 9: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.getString(firebaseData,”IOTLAB/Motor_Control/Motor_Cmd”,s);
s1 = s.substring(2,s.length()-2);
mc = s1.toInt();

## Slide 10
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(20,0,”MOTOR ON”);
display.display();
I2C address
SDA, SCL

## Slide 11: Appliance Control using RTC
RTC – real Time Clock
Turn on an appliance – heater, motor etc- only during a scheduled slot time
The scheduled slot time is settable via a mobile app
Slot time will be stored in the cloud database
RTC with battery backup will be used to get the current time

## Slide 12: DS3231 RTC
Maintains seconds, minutes, hours, days, weeks, months, years information
12 hour/ 24 hour format available for time
Battery back-up so that the clock remains updated even if there is no power
Operating voltage – 2.3V – 5.5V
I2C interface with microcontroller

## Slide 13: DS3231
DS3231 pin | ESP32 pin
SCL | GPIO22
SDA | GPIO21
VCC | 3.3V
GND | GND

## Slide 14
Location on board

## Slide 15: Mobile App

## Slide 16: Basic read
#include <Wire.h>
# include <RTClib.h>
RTC_3231 rtc;
rtc.begin();
rtc.adjust(DateTime(F(_DATE_),F(_TIME)));
DateTime now = rtc.now();
now.hour(), now.minute(),now.second()

## Slide 17: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 18: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.setString(firebaseData,”IOTLAB/Appliance_Control/Current_Time”,s);
Firebase.getString(firebaseData,”IOTLAB/Appliance_Control/Start_Time”,s);
Firebase.getString(firebaseData,”IOTLAB/Appliance_Control/Stop_Time”,s);

## Slide 19
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(0,0,currentTime);
display.drawstring(0,30,startTime);
display.drawstring(80,30,stopTime);
display.drawCircle(60,36,8);
display.display();
I2C address
SDA, SCL

## Slide 20: Biometric based access control
Mobile app with finger print authentication
Authentication status stored in Firebase
GISMO-V reads authentication status and unlocks/locks a solenoid based lock

## Slide 21: Mobile App
Firebase tag : IOTLAB/Lock_Control/Validation_Status

## Slide 22: Home Safety & Security
LPG gas leak sensor MQ6
Magnetic switch to detect door/window open status
The status of the two alerts are transferred to Firebase
Mobile app will display the status of the two alerts

## Slide 23: MQ6 gas leak sensor
FEATURES
* High sensitivity to LPG, iso-butane, propane
* Small sensitivity to alcohol, smoke.
* Fast response .
* Simple drive circuit
APPLICATION They are used in gas leakage detecting equipments in home and industry, are suitable for detecting of LPG, iso-butane and propane

## Slide 24: MQ6
MQ6 pin | ESP32 pin
VCC | 5V
Ground | GND
Digital out | NC
Analog out | GPIO36
Note: There is heater on board which heats the sensor. Stable readings will be got only after about 3 minutes of stabilization after cold start

## Slide 25
Location on board

## Slide 26: Magnetic switch
GND
Internal pullup
Mag sw
ESP32
GPIO16

## Slide 27
Location on board

## Slide 28: Firebase tags
IOTLAB/HSSS/Gas_Leak
IOTLAB/HSSS/Window_Open

## Slide 29: Test Project
Connect a switch to GPIO16
Read switch status
If switch is closed switch on onboard LED else off
Display switch status on OLED